## Slide 1: Omni update
What’s New?
Donald M. Maas, Jr.
Warlord of ingenuity
Mccain, inc.

## Slide 2: Session agenda
What is Omni 2.0?
New file formats/extensions
Installing/databases conversion/How to do it
New remote access username/password
What’s not supported?
What’s new in Omni
Demonstrating new Coord features
Demonstration of peer-to-peer
Omni 101
Ones everyone needs to know about
Bugs (undocumented features)

## Slide 3: Section One what is omni 2.0?
What is Omni 2.0?

## Slide 4: Omni 2.0
2.0 is a major departure from 1.xx.yyyy versions. The file formats for the firmware now use the. mcfw extension and the database goes from .gz to the .mcb extension
The .mcfw file now contains the Linux kernel, BSP (Board Support Package) and the latest Omni release – the new installer program installs and updates all 3
Review of procedure “Updating Omni from Version 1.x.x.x to 2.0.0.0”
New remote access account: omniuser
New password: OmniUserMcCain!Rocks
What’s not supported? Updating F/W through Omni – only through diagnostics

## Slide 5: Section 2.1 Demonstration of Actuated coordination
Live demo

## Slide 6: Actuated coordination
What is actuated coordination?
Actuated coordination is a feature that allows the coordinated phase(s) to ‘gap out’ early if there is no demand on the main street
How is actuated coordination configured in Omni?
There are 3 new parameters in the pattern tables
Use Percent yes/no
Act coord enable yes/no
Act coord value (0-255)
Task: load db file: atcDatabase_1000_01.mcb

## Slide 7: Actuated coordination – normal operation
This database loads 70 seconds cycle, split table 1
1 2 3 4 5 6 7 8
0 35 17 18 0 35 0 0
Omit nact maxv maxv omit nact omit omit
x x
Use Percent no
Act coord enable no
Act coord value 0
Observations:
2/6 fo @ 14 seconds (35-2(r) =33-4(y) =29-15(FDW) =14 sec), phase 3 turns Green @ 35 seconds
Task: load db file: atcDatabase_1000_02.mcb

## Slide 8: Actuated coordination – 5 seconds early
This database loads 70 seconds cycle, split table 1
1 2 3 4 5 6 7 8
0 35 17 18 0 35 0 0
Omit nact maxv maxv omit nact omit omit
x x
Use Percent no
Act coord enable yes
Act coord value 5
Observations:
2/6 Nact drops @ 9 seconds, moves into FDW - (35-2(r) =33-4(y) =29-15(FDW) =14 sec) – 5(AC) = 9 seconds, phase 3 Green @ 30 seconds
Task: load db file: atcDatabase_1000_03.mcb

## Slide 9: Actuated coordination – 5 percent early
This database loads 70 seconds cycle, split table 1
1 2 3 4 5 6 7 8
0 35 17 18 0 35 0 0
Omit nact maxv maxv omit nact omit omit
x x
Use Percent yes
Act coord enable yes
Act coord value 5
Observations:
2/6 Nact drops @ 10.5 seconds, moves into FDW - (35-2(r) =33-4(y) =29-15(FDW) =14 sec) – 5(AC%) = 10.5 seconds, phase 3 Green @ 31

## Slide 10: Section 2.2 Demonstration of Phase reservice
Live demo

## Slide 11: Phase reservice
What is phase reservice?
Phase reservice is a feature that allows the controller to reservice phases multiple times within a cycle if there is unused cycle time.
How is phase reservice configured in Omni?
There are 3 new parameters in the split tables per phase
RSV CNT - max number of times a phase is reserved (0 disables, max is 5 times)
RSV start - time in the local cycle time when phase is eligible for reservice (Seconds or percent)
Rsv end -time in the local cycle time when phase is no longer eligible for reservice (Seconds or percent)
Task: load db file: atcDatabase_1001_01.mcb

## Slide 12: Phase reservice – split side street 3-4 (service on 3 + 4)
This database loads 130 seconds cycle, split table 1
phase 1 2 3 4 5 6 7 8
time 0 65 17 18 0 65 0 0
mode Omit nact minv minv omit nact omit omit
coord x x
Rsv cnt 0 0 0 0 0 0 0 0
Rsv start 0 0 0 0 0 0 0 0
Rsv end 0 0 0 0 0 0 0 0
Observations:
2/6 fo @ 44 seconds (65-2(r) =63-4(y) =59-15(FDW) =44 sec), phase 3 turns Green @ 65 seconds, gaps out and yields to phase 4 @ 73 seconds, gaps out and we return to 2/6 regardless
of demand (minimum recall) on phases 3 and 4
Task: load db file: atcDatabase_1001_02.mcb
Task: load db file: atcDatabase_1001_02.mcb

## Slide 13: Phase reservice split side street 3-4 (reservice on 3 + 4)
This database loads 130 seconds cycle, split table 1
phase 1 2 3 4 5 6 7 8
time 0 65 17 18 0 65 0 0
mode Omit nact minv minv omit nact omit omit
coord x x
Rsv cnt 0 0 5 5 0 0 0 0
Rsv start 0 0 0 0 0 0 0 0
Rsv end 0 0 0 0 0 0 0 0
Observations:
2/6 fo @ 44 seconds (65-2(r) =63-4(y) =59-15(FDW) =44 sec), phase 3 turns Green @ 65 seconds, gaps out and yields to phase 4 @ 73 seconds, gaps out and we start reservice
1st reserve of phase 3 @ 83, gaps – 1st reserve of phase 4 @ 91, gaps
2nd reserve of phase 3 @ 101, gaps – 2nd reserve of phase 4 @ 109, gaps
3rd reserve of phase 3 @ 119, gaps – not enough time for phase 4, back to 2/6 @127
Task: load db file: atcDatabase_1001_03.mcb
Task: load db file: atcDatabase_1001_02.mcb

## Slide 14: Phase reservice split side street 3-4 (reservice on 3 + 4)
This database loads 130 seconds cycle, split table 1
phase 1 2 3 4 5 6 7 8
time 0 65 17 18 0 65 0 0
mode Omit nact minv minv omit nact omit omit
coord x x
Rsv cnt 0 0 5 5 0 0 0 0
Rsv start 0 0 65 65 0 0 0 0
Rsv end 0 0 110 110 0 0 0 0
Observations:
2/6 fo @ 44 seconds (65-2(r) =63-4(y) =59-15(FDW) =44 sec), phase 3 turns Green @ 65 seconds, gaps out and yields to phase 4 @ 73 seconds, gaps out and we start reservice (with windows)
1st reserve of phase 3 @ 83, gaps – 1st reserve of phase 4 @ 91, gaps
2nd reserve of phase 3 @ 101, gaps – 2nd reserve of phase 4 @ 109, gaps
Reservice windows close @ 110, back to 2/6
Task: load db file: atcDatabase_1001_02.mcb

## Slide 15: Section 2.3 Demonstration of peer-to-peer
Live demo

## Slide 16: Peer-to-peer
What is peer-to-peer
Peer-to-peer is a communication application that allows an Omni controller to share up to 32 messages among 8 Peers in a private IP network
How is peer-to-peer configured in Omni?
Plan what task(s) you need to solve with the connection(s)
After the task(s) are defined setup the peer device(s)
After the devices are configured, setup the functions
Test the network communication using Omni’s ‘ping’ utility
Test the peer-to-peek comm using the Omni p2p status display

## Slide 17: Plan what task(s) you want to solve with a p2p connection

## Slide 18: Input the system id and IP address of the peer

## Slide 19
Choose what remote function activates the local operation here we see when peer #1 channel 4 goes green, this controller will trigger preempt detector #3

## Slide 20
Test network connectivity using omni’s ping utility

## Slide 21
Test p2p with peer device status utility

## Slide 22: Section 3 Discussion of bugs/enhancements in 2.0

## Slide 23: Mcom-66
MCOM-66 Issue with pedestrian recycle and MCE (Manual Control Enable)
It was reported that in Omni 1.11.x that if Pedestrian recycle was programmed and MCE was applied that the phase(s) would attempt to clear the ped movement (FDW) and then turn the walk back on – they had to remove the ped recycle programming to get mce to function correctly

## Slide 24: Mcom-67
MCOM-67 Problem exiting Auto Flash to free with detector calls present
Fixed issue where flash would not exit when demand was present later in sequence in the same barrier with the flash entry phase

## Slide 25: Mcom-150
MCOM-150 Disable telnet & ensure ftp and ssh can be enabled/disabled via diagnostics
TELNET/FTP/SSH are now disabled by default
SSH can be enabled/disabled via diagnostics
FTP can be Enabled and disabled. Remote user (even root) can't change directories. The remote user can only see/transfer file from the /mnt/ramfs/hiResData directory
TELNET cannot be enabled via diagnostics. TELNET Cannot be enabled from command line

## Slide 26: Mcom-220
MCOM-220 The webserver should only run https. Remove the ability to run http and free up the port
The web-server will now redirect all traffic from non-secure ports to secure ports
See “not secure” warning after launching
Lorem ipsum

## Slide 27: Mcom-250
MCOM-250 ATC EB-2 Kernel 2.6.22 file-system corruption
Put a jffs2 patch code in the engine board 2 kernel version 2.6.22, 2.422 (EB2, 422) to fix the file system corruption. The garbage collector algorithm changed in the latter kernel version and helped the jffs2 filesystem running smoother
This affects all eB2 applications (McCain, d4, Siemens and econolite)

## Slide 28: Mcom-251
MCOM-251 Allow use of CMU/MMU Field Check even when using custom I/O mapping
When an output is mapped to anything other than a channel driver (Channel Red, Yellow, or Green), such as to a Logic Output, Field Check has to be disabled for said output in the monitor. Created process to look at all possible sources that effect a channel’s assignment and include them in the message to the CMU/MMU.

## Slide 29: Reminder – webserver has separate security enable
In the security options page there is a new field for web UI (Yes/NO)
If active, prompts user for user id and pin